## Slide 1: Variable Length Subnet Mask
Course Code: CSC 3116
Dept. of Computer Science
Faculty of Science and Technology
Course Title: Computer Networks
Lecturer No: | Lab 3 | Week No: | 3 | Semester: | Summer 19-20
Lecturer: | Md. Sakir Hossain, Email: sakir.Hossain@aiub.edu |  |  |  | 

## Slide 2: Lecture Outline
Introduction
VLSM
  Steps of VLSM
  Example 1
  Example 2
3. Homework

## Slide 3: Introduction
A large network is difficult to manage
Less security as each host of the network can reach all other hosts.
Huge broadcast domain, thereby large bandwidth consumption
Waste of unused IP addresses
Problems of Large Network

## Slide 4: Introduction….
Dividing a large network into several smaller networks, called subdivided networks or subnets.
How to overcome the problems?

## Slide 5: Introduction….
For classful addressing
Network | No. of IP addresses allocated
A | 256
B | 256
C | 256
D | 256
E | 256
F | 256
G | 256
Network: E
Required IP: 5
Network: A
Required IP: 56
Network: F
Required IP: 21
Network: G
Required IP: 26
B
C
D

## Slide 6: Introduction
Required IPs: 56+5+21+26+4+4+4=120
Classful address
  No. o allocated IPs: 256×7=1792 IP
  Percentage of unused IP=93% (approx.)

## Slide 7: Introduction
Is there any way to further reduce the unused IP addresses?
Yup!
Instead of giving the same number of IP addresses to all subnets,
allocate different number of IP addresses depending
on the each subnet’s needs.

## Slide 8: VLSM
Variable Length Subnet Mask (VLSM)
Instead of allocating the same number of IP addresses to all networks, the number of IP addresses allocated to network depends on the network’s need.
Different network is provided with different number of IPs

## Slide 9: VLSM
Steps of VLSM
Step 1: Write the networks’ names and IP requirements in descending order of IP requirements.
A (56), G(26), F(21), E(5), B(4), C(4), D(4)
Step 2: Find the number of host bits needed to satisfy the IP requirement of each subnet?
Step 3: Based on the number of host bits, find the subnet mask for each subnet.
Step 4: Allocate IPs to each subnet starting from the beginning of the IP block. Allocate IPs to subnet sequentially according to the sorted network sequence found in Step 1.

## Slide 10: VLSM….
Example 1
Subnet | No. of IPs required | How many bits to borrow | No. of allocated IPs | No. of host bits No. of net bits | Subnet mask | Allocated IP range
A | 56 |  | 64 |  | 255.255.255.192 | 192.168.5.0-192.168.5.63/26
G | 26 |  | 32 |  | 255.255.255.224 | 192.168.5.64-192.168.5.95/27
F | 21 |  | 32 |  | 255.255.255.224 | 192.168.5.96-192.168.5.127/27
E | 5 |  | 8 |  | 255.255.255.248 | 192.168.5.128-192.168.5.135/29
B | 4 |  | 4 |  | 255.255.255.252 | 192.168.5.136-192.168.5.139/30
C | 4 |  | 4 |  | 255.255.255.252 | 192.168.5.140-192.168.5.143/30
D | 4 |  | 4 |  | 255.255.255.252 | 192.168.5.144-192.168.5.147/30
Subnet | No. of IPs required | How many bits to borrow | No. of allocated IPs | No. of host bits No. of net bits | Subnet mask | Allocated IP range
A | 56 |  | 64 |  | 255.255.255.192 | 192.168.5.0-192.168.5.63/26
G | 26 |  | 32 |  | 255.255.255.224 | 192.168.5.64-192.168.5.95/27
F | 21 |  | 32 |  | 255.255.255.224 | 192.168.5.96-192.168.5.127/27
E | 5 |  | 8 |  | 255.255.255.248 | 192.168.5.128-192.168.5.135/29
B | 4 |  | 4 |  | 255.255.255.252 | 192.168.5.136-192.168.5.139/30
C | 4 |  | 4 |  | 255.255.255.252 | 192.168.5.140-192.168.5.143/30
D | 4 |  | 4 |  | 255.255.255.252 | 192.168.5.144-192.168.5.147/30
11111111. 11111111. 11111111. 11000000
26
6

## Slide 11: VLSM….
Example 1
VLSM
  No. of allocated IPs: 64+32+32+8+4+4+4=148 IP
  Percentage of unused IP=% (approx.)
Classful Addressing | VLSM
93% | 19%
Percentage of unused IP address (for the given network)

## Slide 12: VLSM….
Is it possible to further reduce the unused IP?
Spend your time to propose a new subnetting technique.

## Slide 13: VLSM….
Example 2
Suppose that we have three networks: A, B and C with IP requirements 50, 4 and 28. If You are given an IP block 130.3.0.0, allocate IPs performing subnetting.
Subnet | No. of IPs required | How many bits to borrow | No. of allocated IPs | No. of host bits No. of net bits | Subnet mask | Allocated IP range
A | 50 |  | 64 |  | 255.255.255.192 | 130.3.0.0-130.3.0.63/26
C | 28 |  | 32 |  | 255.255.255.224 | 130.3.0.64-130.3.0.95/27
B | 4 |  | 4 |  | 255.255.255.252 | 130.3.0.96-130.3.0.99/30
Subnet | No. of IPs required | How many bits to borrow | No. of allocated IPs | No. of host bits No. of net bits | Subnet mask | Allocated IP range
A | 50 |  | 64 |  | 255.255.255.192 | 130.3.0.0-130.3.0.63/26
C | 28 |  | 32 |  | 255.255.255.224 | 130.3.0.64-130.3.0.95/27
B | 4 |  | 4 |  | 255.255.255.252 | 130.3.0.96-130.3.0.99/30

## Slide 14: Homework
Suppose that we have three networks: A, B and C with IP requirements 500, 4000 and 208, respectively. If You are given an IP block 130.3.0.0, allocate IPs performing subnetting.
Suppose that we have six networks: A, B, C, D, E and F with IP requirements 120, 4 and 9, 4, 32, 7, respectively. If You are given an IP block 210.3.0.0, allocate IPs performing subnetting.

## Slide 15
References
[No reference]

## Slide 16
Recommended Books
  1. Official Cert Guide CCNA 200-301 , vol. 1, W. Odom, Cisco Press, First Edition, 2019, USA.
  2. CCNA Routing and Switching, T. Lammle, John Wily & Sons, Second Edition, 2016, USA.